## Slide 1
Character Writing Robot
Team Details :
Amarjit Prasad (BE-EXTC)
Abhishek Kharche (BE-COMP)
Chinmay Pednekar (BE-COMP)
Vaibhav Naidu (BE-COMP)
SHIVAJIRAO S. JONDHALE COLLEGE OF ENGINEERING
DOMBIVLI
TEAM 6

## Slide 2: Index
Objective
Introduction to Spark V
Custom motor driver
Wireless communication
Programming the motor
Working of mechanism
Character mapping
Simulation
GUI
Applications

## Slide 3: Project objective
  The project objective is to explore the “writing capability of robots”
  We program a Spark V robot ie. ATMEGA 16 based to write on a paper with pen
  A mechanism makes the pen move in different directions
Input is given through user interface using XBEE (Based on zigbee protocol, IEEE 802.15.4)

## Slide 4: Spark V ATMEGA16 Robot
It is based on ATMEGA16 microcontroller.
The robot is equipped with:
3 analog white line sensors,
3 analog IR Proximity sensors,
3 directional light intensity sensors
LCD display
Buzzer
Both serial and wireless communication ports
Has auxiliary and battery power supply
Ultrasonic range sensors (optional)

## Slide 6: Spark V functional block diagram

## Slide 8: ATMEGA 16
It is a 8 bit microcontroller having 40 pins
Has 32 programmable I/O lines split into 4 ports
3 timer pins
Operating voltage is 4.5 to 5.5 V
Dedicated pins for crystal oscillator and reset
Max operating frequency 16MHz
Notes: Timers- 2 8bits and 1 16bit

## Slide 9: L293D motor driver

## Slide 10: ZigBee Advantages
Range is from 30 m to 100 m
Power is 3.3 V
RF Data Rate is 250,000 bps
Retries and Acknowledgements
The XBee/XBee-PRO RF Module is designed to mount into a receptacle (socket) and therefore does not require any soldering when mounting it to a board.

## Slide 11: ZigBee module
ZigBee is a protocol that is based on the 802.15.4 standard
It uses 2.4 GHz band in most of the countries worldwide
Wireless communication occurs in 5 MHz channels ranging from 2.405 to 2.480 GHz
The lower data rate of the ZigBee devices allows for better sensitivity and range
Spark robot has inbuilt pins for mounting zigbee module
It just needs a jumper setting for switching to wireless mode from serial mode

## Slide 12
Serial communication setting
Notes: Baud rate is the speed, daata bits is no of databits in a packet, parity for error checking and correction, handshake, stop bits to indicate end of packet

## Slide 13: Stepper motor
How it works

## Slide 14: Program for Stepper motor
int step = 3;
void stepper(int dir)
{
}
if(dir == 1)
step=4+(step+1)%4;
else
step=4+(step-1)%4;
switch(step)
{
case 4: PORTB |= 0b00001111;
PORTB &= 011111100;
break;
case 5: PORTB |= 0b00001111;
PORTB &= 011111001;
break;
case 6: PORTB |= 0b00001111;
PORTB &= 011110011;
break;
case 7: PORTB |= 0b00001111;
PORTB &= 011110110;
break;
}

## Slide 15: Mechanism

## Slide 16: Line Tracing

## Slide 17: Working
X
Y
L
L = √(X² + Y² )
L1 ² + L ² - L2 ²
cos α = ----------------------
2 L1 L
tan β = X / Y
L1 ² + L2 ² - L ²
cos θm2 = ----------------------
2 L1 L2
θm1 = 180 - α - β

## Slide 18: Character Mapping
X
Y
(0,0)
(50,0)
(50,50)
(50,100)
(0,100)
(-50,100)
(-50,50)
(-50,0)

## Slide 19: Stroke Method

## Slide 20: Example
(50,50)
(50,100)
(0,100)
(-50,100)
(-50,50)
Pen down
Line(-50,100, 0,0)
(0,0)
(50,0)
(-50,0)
Line(0,0, 50,100)
Line(50,100, -25,50)
Line(-25,50, 25,50)
Pen down
Pen up

## Slide 21: Simulation

## Slide 22: GUI
Visual C++
Select COM port at runtime
Check status of robot
Enter multiple characters at a time

## Slide 23
Start
Take next character from input string
Load line coordinates from memory
Proceed to start point and put pen down
Trace inbuilt path to final point and lift the pen
All lines of current alphabet traced ?
Move robot to next position
All characters in input string printed ?
Stop
Flow Chart
Yes
No
Yes
No

## Slide 24: Applications
Large Size Poster Making
License Plate / Vinyl Cutters
Use libraries in future

## Slide 25: Challenges
Notes: Make excuses as to why the project is incomplete :P

## Slide 26: Thank You